## Slide 1: EDESFEM Numerical Analysis Software Specialized for Electrodeposition Coating Simulation

## Slide 2: What is Electrodeposition (ED) ?
Most widely-used anti-rust basecoat methods for various metal products including auto carbodies.
Depositing coating film by applying direct electric current in a paint pool.
Relatively good at depositing a uniform film on bodies in complex shapes.
Cathode
Anode
Paint
＋
http://n-link.nissan.co.jp/
＋

## Slide 3: Importance of ED
Inspections of the safety and structural health of cars (e.g., crash tests) are usually performed with new cars without corrosion.
However, corrosion significantly reduces the strength and stiffness of a car in reality.
In other words, corrosion can easily spoil the value of the inspections with new cars.
ED is critical to the safety and structural health of carbodies.
https://wd40.pk/

## Slide 4: Impact of ED process on carbody design
Undercarriages are exposed to severe corrosive environments. (It is even more severe in environments with seawater or snow-melting chemicals.)
Thus, it is necessary to ensure the ED film thickness is above minimum over the entire surface of the undercarriages.
Some undercarriage parts (e.g., side sills) have bag-like complex structures with laminated plates, making some ED holes as the path for ED current to the inner faces is indispensable.
Side sill
https://www.goauto.ca/
Understanding and considering the ED process, including the location and size of the ED holes, is essential for carbody design.

## Slide 5: Need for ED Simulation
ED holes are essential for corrosion protection, while they are unwanted for strength/stiffness.
Thus, the following conflict occurs in the field of carbody design.
Of course, ED simulation is also useful for pre-study of the effect of ED condition changes on film thickness, cause finding and quick improvement of insufficient deposition, etc..
Corrosion Section
Strength/Stiffness Section
Fewer ED holes!
ED simulation can resolve such conflicts without any seeds of future trouble and lead to the optimal carbody design.
More ED holes!

## Slide 6: What is ED Simulation?
Actual ED Line
ED Simulation
Electrodes (Anodes)
Paint Pool
Carbody w/ Motion
Total length: about 30 m
Paint Pool
Carbody with Motion
Electrodes (Anodes)
are reproduced in a computer.

## Slide 7: What is ES Simulation?
Governing equation: Electrostatic Laplace equation () in the paint pool domain.
Boundary conditions:
  Wall (insulation) BC，
  Anodic (electrode surface) BC,
  Cathodic (carbody surface) BC: Film resistance/growth constitutive model.
Outputs: time-histories of
  Surface potential,
  Current density,
  Film thickness
Identified via lab experiments.
Final film thickness is the main output.

## Slide 8: 4 Features of EDESFEM

## Slide 9: #1: High Accuracy with 4-node Tetrahedral Meshes
S-FEM has recently been put to practical use as a next-gen FEM.
EDESFEM adopts the edge-based S-FEM using 4-node tetrahedral meshes (ES-FEM-T4).
Despite the 4-node tet mesh, superlinear mesh convergence rate is obtained as fast as the 2nd -order elements.
4-node tet meshes enable the analyses with a minimum number of elements, even around ED holes, where the quadratic or Cartesian meshes lead to a massive increase in elements.
Adopting smoothed finite element method (S-FEM) for numerical formulation
Standard FEM
ES-FEM
2D example for simplicity
Putting Gauss point at each element center
Putting Gauss point at each edge center

## Slide 10: #2: Support for Moving Boundary Analysis of Multiple Bodies
The user just needs to prepare the pool/carbody meshes and motion tables for each body.
Using multi-point constraints (MPCs), meshes are automatically connected at interfaces inside EDESFEM.
Inactive Elements
Active Elements of Carbody Mesh
Active Elements of Pool Mesh
Liquid Level
Enabling moving boundary analysis of multiple carbodies with the overset mesh method

## Slide 11: #3: High Speed with MPI/OpenMP Hybrid Parallelization
EDESFEM can use multi-core CPUs in multi-node HPC environments.
Calculation steps:
  Generating T4 mesh for pool and carbody domains.
  Partitioning and reordering each mesh with METIS.
  Preparing an input file containing the mesh filenames, boundary conditions, motion path, etc..
  Executing the program. In the case of OpenMPI: orterun –np 64 -bind-to socket -npersocket 1 -x OMP_NUM_THREADS=8 -x numactl -l edesfem.bin input_file_name.ied
Pool Mesh Partitioning
Carbody Mesh Partitioning
Accepting various HPC environments with MPI/OpenMP hybrid parallelization

## Slide 12: #4: Faithful Reproduction of Deposition Delay on Inner Plates
In ED, the film thickness on the inner plates inside the ED holes is important.
Detailed lab experiments are essential to incorporate the deposition behavior of inner plates into the ED numerical model.
EDESFEM implements ED numerical models obtained from the latest experimental findings.
They contribute to the reduction of non-physical “calibration” work.
Employing the latest ED numerical model based on detailed lab experiments
One-Plate Test
4-Plate Box Test
Circulating Pool Test

## Slide 13: EDESFEM Verification Example 1 4-Plate Box Analysis

## Slide 14: 4-Plate Box Analysis
Outline
Imitating a bag-like structure such as a side sill in a carbody.
Film thickness on the innermost surface (Face G) is the most important so as to guarantee corrosion protection.
The film thickness on Face G is evaluated with 4 different density meshes using FEM-T4 and ES-FEM-T4.
Time-history of film thickness
4 plates form 3 bags.
3rd bag is the most difficult to be deposited.
Photo of a 4-plate box

## Slide 15: 4-Plate Box Analysis
Overview of Meshes
3.2 mm Mesh (about 31k elements)
0.8 mm Mesh (about 169k elements)
1.6 mm Mesh (about 65k elements)
0.4 mm Mesh (about 716k elements)
Only the surface meshes are shown.

## Slide 16: 4-Plate Box Analysis
Film Thickness on Face G (innermost surface)
FEM results (dashed lines) have significant errors.
Meanwhile, ES-FEM results (solid lines) have no such errors due to the fast mesh convergence rate.
Mesh size

## Slide 17: 4-Plate Box Analysis
Comparison of Mesh Convergence Rate on Face G (innermost surface)
FEM-T4 shows a linear convergence.
EDESFEM (ES-FEM-T4) shows a quadratic convergence.
ES-FEM-T4 adopted by EDESFEM has a much faster mesh convergence rate than the standard FEM-T4.
The result of ES-FEM with the finest mesh (0.4 mm) is used as the reference.
In Final thickness

## Slide 18: 4-Plate Box Analysis
Comparison of Calculation Time
on a PC (only 1 CPU: 16 cores of Intel i9-9960X)
With the same mesh, ES-FEM-T4 is slower than FEM by x2 3.
For the same accuracy, ES-FEM-T4 is faster than FEM by x4.
Mesh Size | Standard FEM (FEM-T4) | EDESFEM (ES-FEM-T4)
3.2 mm | 7 s | 10 s
1.6 mm | 8 s | 14 s
0.8 mm | 12 s | 26 s
0.4 mm | 41 s | 125 s
Comparable Accuracy
ES-FEM-T4 adopted by EDESFEM is supremely efficient in comparison to FEM-T4.

## Slide 19: EDESFEM Verification Example 2 Actual Line Analysis

## Slide 20: Actual Line Analysis
Outline
Half-body analysis (only right-hand side).
Entire line shape, carbody motion, and electrode conditions are faithfully reproduced.
About 1000 timesteps for 300 s (i.e., average s).
The film thickness distribution is evaluated with 3 different density meshes using FEM-T4 and ES-FEM-T4.

## Slide 21: Actual Line Analysis
Overview of Surface Mesh of 10M Element Mesh
There are many ED holes around narrow spaces among plates.
Only the surface mesh is shown.

## Slide 22: Actual Line Analysis
Overview of Surface Mesh of 16M Element Mesh
There are many ED holes around narrow spaces among plates.
Only the surface mesh is shown.

## Slide 23: Actual Line Analysis
Overview of Surface Mesh of 51M Element Mesh
There are many ED holes around narrow spaces among plates.
Only the surface mesh is shown.

## Slide 24: Actual Line Analysis
Animation of Surface Potential (EDESFEM with 51M Element Mesh)
Outer View Inner View

## Slide 25: Actual Line Analysis
Animation of Current Density (EDESFEM with 51M Element Mesh)
Outer View Inner View

## Slide 26: Actual Line Analysis
Animation of Film Thickness (EDESFEM with 51M Element Mesh)
Outer View Inner View

## Slide 27: Actual Line Analysis
Film Thickness Distribution on the side sill part with 51M Element Mesh
Standard FEM (FEM-T4)
EDESFEM (ES-FEM-T4)
Reference Solution
Standard FEM shows a little thicker result. (The center of the side sill is Yellow.)
This result is regarded as the reference solution. (The center of the side sill is Green)

## Slide 28: Actual Line Analysis
Film Thickness Distribution on the side sill part with 16M Element Mesh
参照解
Standard FEM shows a much thicker result. (The center of the side sill is Orange.)
EDESFEM shows an accurate result. (The center of the side sill is Green.)
Standard FEM (FEM-T4)
EDESFEM (ES-FEM-T4)

## Slide 29: Actual Line Analysis
Film Thickness Distribution on the side sill part with 10M Element Mesh
参照解
Standard FEM shows a massively thicker result. (The center of the side sill is Red.)
EDESFEM shows a little thicker result. (The center of the side sill is Yellow.)
A comparison of the time-history of the film thickness at this point is shown on the next page.
Standard FEM (FEM-T4)
EDESFEM (ES-FEM-T4)

## Slide 30: Actual Line Analysis
Comparison of Time-histories of Film Thickness at a Sample Point on Side Sill
FEM-T4 with 51M elems. and ES-FEM-T4 with 10M elems. has almost comparable accuracy.
ES-FEM-T4 with 16M elems. gives a practically converged result.

## Slide 31: Actual Line Analysis
Comparison of Calculation Time
On a cluster (64 CPUs: 896 cores of Intel Xeon E5-2680 v4 on TSUBAME3.0)
With the same mesh, ES-FEM-T4 is slower than FEM by x1.5.
For the same accuracy, ES-FEM-T4 is faster than FEM by x3.
# of Elements | Standard FEM (FEM-T4) | EDESFEM (ES-FEM-T4)
10M | 1.6 h | 1.9 h
16M | 2.3 h | 3.4 h
51M | 6.0 h | 8.5 h
Comparable Accuracy
For the simulations of actual ED lines with parallel computing, ES-FEM-T4 adopted by EDESFEM is much more efficient than FEM-T4.
An actual line analysis of a single-body entry takes only a few hours.

## Slide 32: Actual Line Analysis
Strong Scaling Test (with 10M Element Mesh)
On a cluster (up to 64 CPUs: 896 cores of Intel Xeon E5-2680 v4 on TSUBAME3.0)
EDESFEM scales to some extent up to 64 CPUs at least.

## Slide 33: EDESFEM Validation Example 1 4-Plate Box Test/Simulation

## Slide 34: 4-Plate Box Test/Simulation
Overview
Paint
Box
Constant-Temp. Water Bath
Cylibder (Anode)
The Box
Overall view
Plates(Cathode)
Spacer
Spacer
Spacer

## Slide 35: 4-Plate Box Test/Simulation
Validation of Surface Potential (left) and Current Density (right)
The simulated results are agreed with the experiment results in practical accuracy.

## Slide 36: 4-Plate Box Test/Simulation
Validation of Film Thickness
Although the accuracy of the innermost surface (G-Face) remains an issue (maximum error of 3 μm), the accuracy of the other surfaces is practically enough (less than 2 μm error).

## Slide 37: EDESFEM Validation Example 2 Actual Line Test/Simulation

## Slide 38: Actual Line Test/Simulation
●
●
●
●
●
Ch.2：Hood
Ch.4：Roof
Ch.3：Side Door
Ch.5：Side Sill
Ch.7：Back Door
Ch.6：Floor (not visible on this Fig.)
Outline Measured 6 Points
Test
A surface potential measurement device with 6 probes was mounted on a car running on an actual line to measure surface potential.
After baking, the film thickness was measured at the 6 points.
Simulation
Half-body analysis considering the right-hand side of the pool and car.
Shapes of the pool, electrodes, and carbody with motion are reproduced.
Surface potential time histories and final film thickness at the 6 points are compared.

## Slide 39: Actual Line Test/Simulation
Validation of Surface Potential (Ch. 2 and 3)
The simulated surface potential is a little high because the degradation of the membranes of electrodes was not precisely simulated; yet, the results generally agree with practical accuracy.

## Slide 40: Actual Line Test/Simulation
Validation of Surface Potential (Ch. 4 and 5)
The simulated surface potential is a little high because the degradation of the membranes of electrodes was not precisely simulated; yet, the results generally agree with practical accuracy.

## Slide 41: Actual Line Test/Simulation
Validation of Surface Potential (Ch. 6 and 7)
The deposition delay at the floor, an inner part, is reproduced successfully.
The simulated surface potential is a little high because the degradation of the membranes of electrodes was not precisely simulated; yet, the results generally agree with practical accuracy.

## Slide 42: Actual Line Test/Simulation
Validation of Film Thickness
Point | Measured () | Simulated () | Error ()
Ch.2: Hood | 20.1 | 21.4 | 
Ch.3: Side Door | 19.0 | 21.0 | 
Ch.4: Roof | 17.0 | 19.3 | 
Ch.5: Side Sill | 20.0 | 21.6 | 
Ch.6: Floor |  | 14.5 | 
Ch.7: Back Door | 23.0 | 20.3 | 
Point |  |  | 
Ch.2: Hood | 20.1 | 21.4 | 
Ch.3: Side Door | 19.0 | 21.0 | 
Ch.4: Roof | 17.0 | 19.3 | 
Ch.5: Side Sill | 20.0 | 21.6 | 
Ch.6: Floor |  | 14.5 | 
Ch.7: Back Door | 23.0 | 20.3 | 
Although there is still room for improvement in accuracy, the maximum error in film thickness is less than 3 , which is accurate enough for practical use.

## Slide 43: EDESFEM Summary

## Slide 44: Summary
The electrodeposition simulator “EDESFEM” is now on sale.
4 features of the software were introduced:
  High Accuracy with 4-node Tetrahedral Meshes,
  Support for Moving Boundary Analysis of Multiple Bodies,
  High Speed with MPI/OpenMP Hybrid Parallelization,
  Faithful Reproduction of Deposition Delay on Inner Plates.
V&Vs for the 4-plate box and an actual line were presented.
Please feel free to contact us at the following e-mail address for trial or purchase of EDESFEM or for any questions.
We also welcome your inquiries about ED lab experiments and actual line measurements.
edesfem@rccm.co.jp
Leaflet is also available!
Search
edesfem